## Slide 1
Electron
Paramagnetic
Resonance (EPR)
at X- and W-band
Frequencies
at the University of Alabama

## Slide 2
R
Medicine
Material
research
Physics
Chemistry
Biology
EPR provides detection and study of
radicals (R), systems containing
unpaired electron spins
 Polymers
 Fullerenes
 Glasses
 Corrosion
 Magnetic susceptibility
 Semiconductors
 Defects in crystals
 Quantum dots
High T
superconductors
 Oxidation and reduction processes
 Biradicals and triplet state molecules
 Reaction kinetics
 Structure, dynamics, and reactions
of polymers
 Photosynthesis
 Protein labeling
 Enzymatic reactions
 Metallo-enzymes
 Control of irradiated
food
 Free radicals in living
tissue
 Radical-initiated
carcinogenesis
 Oxygen concentration
measurement
 Spin trapping of
short-lived radicals

## Slide 3
Magnetic Resonance Condition
B0
N
S
N
S
The electron has a magnetic moment:
e = gS
g factor = 2.0023 for free electron
- Bohr magneton
S = ½ - electron spin
ms = - ½
ms = + ½
In magnetic field, B0
ms =  ½ - projection of the electron spin
(S) on the direction of the
magnetic field
E = - e B0 = g B0 ms =  ½ g B 0
-1/2 gB0
+1/2 gB0
B = 0 B > 0
E
h = gB0
A peak in the absorption occurs
when the energy difference between
two levels (gB0) matches
the energy of irradiation (h)

## Slide 4: h = gBr
Frequency EPR 103 > NMR (GHz vs MHz)
Coupling EPR 106 > NMR (MHz vs Hz)
Relaxation EPR 106 < NMR (ns vs ms)
Sensitivity EPR 106 > NMR
In EPR experiment we keep the radiation frequency constant
and scan the magnetic field

## Slide 5
The general outlay of an EPR spectrometer
Magnet
MW Bridge
Cavity
Console
Signal Processing &
Control Electronics
Signal
channel
Field controller

## Slide 6
Frequency band MW Frequency Magnetic Field Sample tube o.d.
GHz mT mm
X 9.2 330 4
Q 35 1200 2
W 94 3300 0.9
Available at the University of Alabama

## Slide 7: What kind of information can we extract from EPR spectrum?
The integrated intensity of the EPR signal
- Concentration
g – Value – a “fingerprint” of the radical;
electronic structure and symmetry
giso
gII
g
I
gX
gY
gZ
Spheric
Rhombic
Cylindrical

## Slide 8
Multiplet Structure
Hyperfine interactions (HFI)
Zero-field interactions
Dipole-dipole interactions
HFI splits EPR line into (2nI + 1) lines, were
I is a nuclear spin, n – number of equivalent nuclei
aH
aN
Nitroxide: 1N (IN = 1)
Quinone: 4 protons (IH = ½)

## Slide 9
ENDOR (Electron Nuclear Double Resonance)
provides missing information
        A) For many biological systems with small hfc constants which are not resolved in EPR spectrum:
P700 radical cation
(Chl a dimer)
EPR
ENDOR

## Slide 10
B) If number of EPR lines are too large to make an analysis
For an electron spin S = ½ coupled to N nuclear spins I = ½,
EPR spectrum consists of 2N lines, whereas ENDOR spectrum
exhibits only 2N lines.
MS = 1
MI =  0
MS =  0
MI =  1
EPR
ENDOR

## Slide 11
NMR = n  a/2
A1
A2
EPR
ENDOR
Phenalenyl radical
Hyperfine enhancement effect

## Slide 12: Why use higher frequencies? 95 GHz and >
To increase sensitivity
To improve g-tensor resolution
95 GHz
TEMPONE
gXX
gYY
gZZ
9 GHz
MYOGLOBIN
gII
gI

## Slide 13
To separate radicals with close g values:
H =
h g
g(g + g)
By increasing frequency ,
we can make H greater
than the linewidth.
To improve resolution for high spin systems with large ZFS
To measure relaxation times (higher frequencies
are often more sensitive to fast molecular motions than lower
frequencies
Fe3+ (S = 5/2)
9 GHz
ZFS>h
109 GHz
h>ZFS

## Slide 14: Why use pulse EPR?
Structure and location of catalytically active species on high-surface area solids and within molecular sieves. Structural environment of Men+ centers - ESEEM
Radicals and paramagnetic transient metal complexes in biological systems - pulse ENDOR
NO-Fe2+ heme protein interactions - HYSCORE (to distinguish between pyrrole Ns and ligand Ns)
Measuring spin-spin distances - DEER (protein labeling), out of phase ESEEM (photochemically generated radical paires, P+700A-1; P+865Q-A)
Direct measuring of T1 and T2 relaxation times.

## Slide 15
Z
Y
X
B0
/2

echo


2-pulse spin echo sequence
(Hahn echo)
Z
Z
Z
X
X
X
Y
Y
Y
/2


## Slide 16: Transient EPR of Light-Induced P700+A1- Radical Paires in Photosystem I
Transient EPR spectrum recorded for a fixed time window after the laser pulse
Transient signal S(t) at fixed
magnetic field values

## Slide 17
Bruker ELEXSYS E-680 W/X system